Sniffer Reactor
The Sniffer Reactor captures and decodes traffic from network interfaces. This can be live traffic traveling through a network in real time or previously captured traffic stored in a standard PCAP format. The Sniffer Reactor understands any network protocol for which you have installed a Pion plug-in (for example plug-ins are available for the HTTP, HTTPS, and SMTP protocols). With the proper plug in, Pion can see and understand traffic on the network, such as traffic between web servers and clients, and can generate events based on that traffic.
When you first add a the Sniffer Reactor you will be prompted for the following fields:

Field	Description
Name	Specify the name of this Sniffer Reactor. This can be any name you find descriptive, we recommend something which describes the network segment to which this Sniffer Reactor is listening.
Comments	Enter some descriptive comments about this Sniffer Reactor. Any comment you feel will help you in the future, we recommend choosing something that includes the contact person for the network segment and any associated work code that may be needed in the future.
Protocol	From this drop down list, select the protocol you want the Sniffer Reactor to use when listening to traffic. By default Pion supports the following protocols: / HTTP (no content) captures the critical fields needed by web analytics tools. These fields include those pertaining to URL, host, referrer, page title, user agent, cookie and query. / HTTP (full content) captures the critical fields needed by web analytics tools, and also captures the page content and the full client request. / Page content (from the request and the response) is saved into a special field in the clickstream term called sc-content. The maximum amount of data in sc-content can be defined in the Protocol configuration. The default is 512k for sc-content. / The client request is saved into a special field in the clickstream term called cs-content. / Note that capturing using the HTTP (full content) protocol requires more memory than capturing using the HTTP (no content) protocol. More memory is required because more data must be captured and manipulated, and because the amount of data making up page content is often much more than any other field. / SMTP captures the critical fields from SMTP-based emails, allowing you to generate events based on emails. All standard SMTP header fields and the message body are captured. / The maximum amount of data stored from the message body can be defined in the Protocol configuration (the default is 1MB). / The default is HTTP(full content) because it contains all of the information, if you are limited in memory or don’t need page content then it can be easily switched to improve performance.
Num Processing Threads (Number of Processing Threads)	Specify the number of processing threads a Sniffer reactor uses. It is useful for provisioning resources on the Pion server or in a shared environment. Adding more available processing threads can improve the performance of Pion significantly on machines with multiple processing cores. / Note: Generally you should not use more threads than you have CPUs/Cores in the Pion server.
Queue Event Delivery	Fill this check box to cause events to be delivered to other reactors by threads not affiliated with this reactor (other threads in Pion). Enabling this feature distributes workload and adds an additional memory-based work queue, which may reduce overall performance. / If this check box is empty, the feature is disabled and the processing threads of this reactor also handle the delivery of events to other reactors. Disabling this feature may improve overall performance because there will be less context switching.
Maximum packet queue size	Specify the maximum number of packets that can be in the event queue per processing thread. We recommend that the total (this value * number of processing threads) be between 200,000 and 300,000. / Note that the queue size setting has a direct impact on possible memory consumption, and that it also determines how much you can buffer in a burst. You must set the queue size to balance between these considerations according to your needs and resources.

Once the Sniffer Reactor has been added to the workspace it must be configured to listen to network traffic. By double clicking on the reactor you will open the following configuration screen:

In addition to the fields you saw when adding the reactor initially you will see sections for Captures, SSL Servers and Connections.
The Captures Section
This section specifies where your Sniffer Reactor will be getting data from. Each line represents a data source and a filter to be applied to that data source. There are two types of supported data sources; Interfaces and Capture Files.
Field	Description
Interface	Specifies the network interface to use when listening to traffic. / Select the cell in the Interface column to display an automatically populated drop down list of the network interface cards on the Pion server. You can then choose the interface that is receiving the live traffic you want to listen to. / Interfaces include: / eth0 / eth1 / ethX (Ethernet interfaces) / wlan0 (or similar, wireless interfaces) / lo / lo0 (or similar, often "loopback" devices) / Note: If you are running VMware, there will be many other virtual interfaces, between the VM and the host. / To see the devices, their IP addresses, and other interface information: / On Windows operating systems, run the command "ipconfig /all". / On Unix-based operating systems, run the command "ifconfig -a".
Capture File	Specifies a file that contains saved traffic. This content of the file will be used instead of live traffic from an interface. / If the traffic has already been captured in a file, simply type the full file path in the Capture File column (note: the file must be a standard .cap or .pcap file).
Filter	Defines the filters to apply to the traffic received on the interface specified above. / After selecting your traffic sources, you can filter out traffic which Pion doesn’t need to see. Although traffic can be filtered out later using other reactors, doing it at this stage as part of the Sniffer Reactor is the most efficient way to remove unwanted information. The filter reactor uses the same syntax as the tcpdump utility. For example if you only wanted normal HTTP traffic you would use “tcp port 80” as your filter string to remove all non HTTP traffic. Complete tcpdump syntax can be found at http://www.tcpdump.org/tcpdump_man.html.

Click on the ADD NEW CAPTURE icon to add a new line to the table.
To delete a capture, click on the “x” at the end of the row describing that capture.
The SSL Servers Section
This section is used only for sites that use SSL encrypted communications such as those common in retail, defense, and financial applications. Pion is able to decrypt data in real-time provided it has the proper keys.
To specify an SSL server, simply click the ADD NEW SSL SERVER icon and specify the following:
Field	Description
Address	The IP Address or DNS name of the SSL server.
Port	The value specified is used in conjunction with the Address (above) to determine if the traffic is encrypted using the provided keyfile (below).
Keyfile	The path to the SSL key file. This path must be relative to the Pion server to ensure proper access. The key can be any standard PEM formatted file.

To delete a server, click on the “x” at the end of the row describing that server.

The Connections Section
The Connections section describes input and output connections for this Sniffer Reactor. See Error: Reference source not foundX on page XError: Reference source not foundX for more information.